## Slide 1: Quantum Mechanical Correction of Lennard Jones Potential Parameters for Towhee Simulations
Om Mihani & Shreya Makkar

## Slide 2: INTRODUCTION
Hydrogen is a promising new fuel for automobiles
A major difficulty is storage
  Containers weigh and cost much more than the fuel itself
Use of Hydrogen Hydrates in ice is a new-and-coming idea
It has environmental advantage over MOFs, COFs, MHs, etc.

## Slide 3: OBJECTIVE
To Change Lennard Jones potential without changing its functional form
To match modified force field with quantum Feynman-Hibbs formulation
Using accurate expression is very computationally expensive, a simplified approach can curb that

## Slide 4: METHODOLOGY
Comparison of Quantum and Classical fields: Quantum has a shallower well and Rmin is shifted rightwards
Change epsilon and sigma parameters to approximately match Feynman-Hibbs potential graph
Inspiration from literature for corrections in epsilon and sigma
Lennard Jones Potential Function
Feynman–Hibbs effective
quantum potential

## Slide 5: METHODOLOGY
Observed that graph has correct minima position, but the well is too deep
Used a (1+α) factor to account for the extra depth
Initially, α obtained analytically from the equations
But, observed that numerical methods do a much better job
Alpha found using minimization of area between r = σ and r = 1.5 σ
Values validated using Energy Minima of new graph and quantum graph

## Slide 6: RESULTS

## Slide 7: CONCLUSIONS
Through a simplified approach we are able to capture quantum effects in the effective force field
Further scope: Cage occupancy of hydrates structures can be calculated, and effect of quantum model can be determined, useful in practical applications of hydrogen fuel

## Slide 8
THANK YOU