## Slide 1: Oscillating Oxidation of Formic Acid
Electrochemical Modelling Project
By Om Mihani
4th March 2025

## Slide 2: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
Image Source: Wikipedia
FORMIC ACID
CARBON MONOXIDE
CARBON DIOXIDE

## Slide 3: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE PHENOMENA
FORMIC ACID ELCTROCHEMICAL OXIDATION

## Slide 4: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE PHENOMENA
FORMIC ACID ELCTROCHEMICAL OXIDATION
Reactions
HCOOH ⇄ CO (adsorbed) + H2O
CO + H2O → CO2 + H2 + 2e-

## Slide 5: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE MODEL
BULK DIFFUSION OF FORMIC ACID
Reasons:
Keeps concentration in bulk constant
Allows finite domain oscillations
Defines a length scale

## Slide 6: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE MODEL
SURFACE COVERAGE OF CO

## Slide 7: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE MODEL
SURFACE COVERAGE OF CO
Note:
The unit for k1 is not sec-1. It is m/s

## Slide 8: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE MODEL
SURFACE COVERAGE OF CO
Note:
The unit for k1 is not sec-1. It is m/s
Reasons:
To make the LHS dimensionally consistent
To express surface reaction instead of bulk
To show dependance on availability of sites
To inculcate oxidation via electricity

## Slide 9: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE MODEL
BUTLER VOLMER KINETICS WITH A TWIST
Reason:
BV kinetics can be used to model both fast and slow Electron transfer

## Slide 10: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE MODEL
BUTLER VOLMER KINETICS WITH A TWIST
Reasons:
Theta denotes the dependance on surface coverage
F considers the hysteresis Function
K2 gives the oxidation kinetics

## Slide 11: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE MODEL
BUTLER VOLMER KINETICS WITH A TWIST
Note: First time ever used Hysteresis expression for Formic acid oxidation

## Slide 12: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE MODEL
BOUNDARY CONDITIONS
DIRICHLET BOUNDARY
NEUMANN BOUNDARY

## Slide 13: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE MODEL
INITIAL CONDITIONS

## Slide 14: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE CASES
5 CASES

## Slide 15: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE SOLUTION
CASE 1: THE LOGIC
Assumption:
Diffusion is much faster than the surface reaction.
Test:
Taking typical values,
Tdifusion = 0.1 s
Treaction = 1 s
This allows:
PDE -> ODE
How:

## Slide 16: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE SOLUTION
CASE 1: THE MATH

## Slide 17: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE SOLUTION
CASE 1: THE MATH

## Slide 18: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE SOLUTION
CASE 1: THE MATH

## Slide 19: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE SOLUTION
CASE 1: THE RESULTS

## Slide 20: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE SOLUTION
CASE 1: THE RESULTS

## Slide 21: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE ANALYSIS
CASE 1: THE ANALYSIS
The Bifurcation Diagram
Food for thought: Why doesn't Surface Coverage ever exceed 0.5 while it goes below 0.1?

## Slide 22: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE ANALYSIS
CASE 1: THE ANALYSIS
The θ time profile
Note:
θon = 0.5 and θoff = 0.1
5 Regimes:
Regime 1: Complete Saturation (𝜂 = 0)
Regime 2: Partial Saturation (0 < 𝜂 ⩽ 0.11)
Regime 3: Bounded Oscillations (0.12 ⩽ 𝜂 ⩽ 0.21)
Regime 4: Overshooting Oscillations (0.22 ⩽ 𝜂 < 0.3)
Regime 5: Boundary Oscillations (0.3 ⩽ 𝜂)
Note 2: As θ increases in regime 3, the frequency of oscillations increases

## Slide 23: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE ANALYSIS
CASE 1: THE ANALYSIS
The Concentration-Space profile
We then consider an overshooting case (𝜂 = 0.25) and observe how concentration varies across space

## Slide 24: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE ANALYSIS
CASE 1: THE ANALYSIS
The Concentration-Space profile
KEY POINT: We considered dC/dt = 0 however, it clearly changes with time.
This approximation could only be made based on the argument that Diffusion is faster than Surface deposition. However, this is still an approximation and will be dropped in subsequent cases.

## Slide 25: INDEX
The Phenomena
The Model
The Cases
The Solution
The Analysis
The Future
THE FUTURE
Solving Cases 2-5
Establishing existence of resonance
Application to analytical measurements

## Slide 26: CREDITS
PROFESSOR BEN JOHNSON
JIXIA LU
PERPLEXITY AI:
  Used for literature Review
  Help in code writing
  Brain storming